|  | ......................... pcs. .............................. € .............................. € GEZE TSA 395 revolving door system in 3 or -4 leaf version With freely selectable outer diameter up to 6000 mm, TÜV type-tested in accordance with EN 16005, with fine frame inviting design and many possible configuration options. Drive types ( ) fully automatic GEZE revolving door system (triggered via movement detector) PLC controlled, electromechanical drive with infinitely adjustable speed, drive with two pre-set speeds. Complete drive with control unit on the interior, control unit in performance level "c" in accordance with DIN EN ISO 13849-1, convenient parameter setting, commissioning and maintenance via service terminal, power supply: 230 V / 50 Hz / 350 W / 10 A, programme switch to select the mode of operation integrated at the post Fuse protection in accordance with EN 16005 (TÜV type-tested and certified) comprising: - Post safety - Emergency push button DIN EN ISO 13850 - Front post safety (non-contact) - Safety contact strip on the leaf, horizontal (heel protection) - Safety contact strip on the leaf, vertical (hand protection) - Mobile safeguarding device on the leaf Construction dimensions: ( ) inner diameter: .................. ... mm (…) ( ) outer diameter:.. ..................mm (freely selectable between 4000 and 6000 mm) ( ) clear passage height DH: .... .. mm (up to 3000 mm, higher on request) ( ) Total height of door system: ...............mm ( ) floor recess: ................ ..........mm (min. 40 mm) Note: Other dimensions on request. Door position: ( ) central ( ) off-centre, offset in relation to the façade ….. Model type: ( ) 3-leaf ( ) 4 leaf ( ) with showcase Turnstile: ( ) rigid door leaves, fine-framed for mounting LSG 8 mm glass. or ( ) break-out/swivelling leaf suitable for use in escape and rescue routes and for ventilation purposes. Note: A suitable escape and rescue route is only achieved from an inner diameter of 2600 mm. Max. wind load 6 Beaufort. (Only suitable for automatic doors) Note: Local building legislation must be complied with! Fine-framed drum walls made of aluminium profiles for mounting: ( ) curved LSG 8 mm, clear Aluminium ceiling construction: ( ) 400 mm standard height or ( ) raised ceiling canopy .............mm, with perimeter canopy cover made of curved aluminium sheets Roof covering outside: ( ) metal cover plate or ( ) waterproof roof with 2 water spouts (flat roof without gradient) Roof covering inside: ( ) metal cover plate Soffit: ( ) consisting of aluminium circle elements in system colour incl. inspection opening Surface of the light alloy parts: ( ) powder coating according to RAL or ( ) LM anodised E6/EV1 or ( ) colour anodised ............ or ( ) coated with ground stainless steel, grain 240 or ( ) coated with polished stainless steel or ( ) coated with stainless steel in special design …………. Floor ring ( ) GEZE 360° stainless steel (V2A) floor ring made of rectangular tubing 40x20x2 mm. The floor ring is used as the floor covering edging at the same time. ( ) Sheet metal base 100 mm or ( ) direct installation of the self-supporting drum construction to the top edge of the finished floor. Note: Only possible with sufficient load-bearing and plane finished floor. Not possible for versions with break-out/swivelling leaves. Note: The insulation of the building must be carried out on site. Floor cover ( ) GEZE scraper mat, black, 20 mm, more colours available on request! or ( ) floor cover to be carried out on site Delivery and installation Wiring to be carried out on site according to the GEZE cable plan by an electrical contractor. Installation, commissioning and instruction of the operator as well as documentation handover in compliance with EN 16005 through plant fitters or service partner. In compliance with EN 16005: - Safety analysis must be carried out as a basis for planning and execution - An inspection must be carried out at least 1 x year and after-sales service maintenance at least 1 x year |
| --- | --- |
|  | ......................... pcs. .............................. € .............................. € Night-time closer (optional position) ( ) GEZE night-time closer sliding doors running on the outside, manual, closing possible from the inside and outside. ( ) fine-framed in LSG 8 mm, clear Locking of the night-time closer sliding doors using: ( ) hook bolt lock |
|  | ......................... pcs. .............................. € .............................. € Locking door leaves (optional position) ( ) without locking mechanism or ( ) manual locking using GEZE bolt lock mounted on the door leaf or ( ) automatic bistable GEZE motor lock Note: When using sliding doors with night-time closers, the turnstile does not need to be locked |
|  | ......................... pcs. .............................. € .............................. € Push pad (optional position) ( ) Delivery and installation of two GEZE push pads with wheelchair symbol on the post of the revolving door. When this push pad is activated, the revolving speed is reduced to an adjustable value to allow disabled persons a higher degree of access convenience and more safety. The activation duration can also be adjusted. |
|  | ......................... pcs. .............................. € .............................. € Lighting (optional position) ( ) ..... pcs. LED spotlights (max. 10 W per light) integrated in the soffit or ( ) ..... pcs. recess for on-site lights (diameter = ..... mm) |
|  | ......................... pcs. .............................. € .............................. € Hot-air curtain system (optional position) ( ) hot-air curtain system integrated in the suspended ceiling construction of the revolving door incl. blow-out channel in the canopy area. Minimum canopy height 400 mm, depending on diameter. Hot-air curtain system design with: ( ) electric connection: Heat output: ............kW/amount of air.........m³/h ( ) hot water connection: Heat output: ............kW/amount of air.........m³/h Note: The power of the hot-air curtain equipment included in the offer has not been calculated by us; the dimensioning and specification of the hot-air curtain must be carried out by the specialist planner responsible. |
|  | ......................... pcs. .............................. € .............................. € Façade connection ( ) GEZE ….. mm panel ( ) installed on site with GEZE side connection profile |