|  | ......................... pc € .............................. € .............................. Panic lever lock set GEZE IQ lock EM Self-locking panic lever lock GEZE IQ lock EM for single-leaf doors tested and approved to EN 179 and EN 1125! Panic unlocking via latch or panic bar; changeover function for unlocking from outside Divided and separated cross latch for absolute unencumbered crossbar projection without jamming even when preloaded! The electrically connectable exterior handle (fail secure version) facilitates unlocking from the outside. Daytime operation with permanently open position can be achieved through permanent coupling of the exterior handle. Combines therefore well with access control systems. All required contacts are integrated in the lock and provide potential-free feedback: Deadbolt contact (with 95 % crossbar projection) Latch contact (with latch activation on the panic side 10°) Cylinder contact Auxiliary lock contact (door open/door leaf enclosed) Release contact (exterior handle engaged) Prepared for installation of profile lock cylinders and with 9 mm square nut. Closed and corrosion-resistant steel lock case in DIN sizes, front plate in stainless steel For use in escape and rescue routes or in fire protection doors, fittings are required in accordance with EN 179 or EN 1125:. For approved fittings, please refer to the currently valid certificate versions0757-CPR-229-7013137-5-2 / 0757-CPR-229PANIK-7013137-4 to certify the durability. Only GEZE components tested and approved together in accordance with EN 179 and EN 1125 may be installed! Please see the following EC certificates of conformity for approved fittings: 0757-BPR-229-09-003 / 0757-BPR-229-09-004 Nominal voltage: 24 V DC Current consumption: 210 mA Supplied in a set comprising: 1 pc lever mortise lock IQ lock EM with lock plate 1 pc connecting cable 12-core; 10m 1 pc cable duct open ( ) door leaf DIN right opening outwards / DIN left opening inwards ( ) door leaf DIN left opening outwards / DIN right opening inwards ( ) IQ lock EM 9235 (distance 92 mm, backset 35 mm) ( ) IQ lock EM 9240 (distance 92 mm, backset 40 mm) ( ) IQ lock EM 9245 (distance 92 mm, backset 45 mm) ( ) IQ lock EM 7255 (distance 72 mm, backset 55 mm) ( ) IQ lock EM 7265 (distance 72 mm, backset 65 mm) ( ) IQ lock EM 7280 special backset 80 mm ( ) IQ lock EM 7210 special backset 100 mm Accessories: ( ) 1 pc. power supply 24 V DC part no. 109637 ( ) 1 pc. GEZE panic bars (EN 1125) configurable part no. 119005 To ensure all functions of the IQ lock EM a door closer is to be fixed to the door. ( ) 1 pc. TS 5000 part no.027333 |
| --- | --- |